## Slide 1: CanberraUAV Workshop Ground Control Stations
Feb 2017

## Slide 2: Ground Control Stations
Also known as GCS
Communicate with the UAV
Receive telemetry data
Send commands to UAV

## Slide 3: GCS -Introduction
Telemetry Data
  Data sent from UAV to GCS
  Contains information about the current state of the UAV
    Speed
    Position
    Altitude
    System errors

## Slide 4: GCS -Introduction
Command data
  Data sent from GCS to UAV
  Can be
    Flight commands (RTL, Goto waypoint)
    Get/set flight parameters
    Get/set mission waypoints

## Slide 5: GCS -Introduction
A GCS Consists of
  Communications Link
  GCS Computer
  GCS Software
  Other accessories - live video feed, tracking antenna, DGPS base station, etc as required

## Slide 6: GCS - Software Options
Most GCS software is run on laptops
Different options depending on
  Which flight controller is used
  GCS Operating System
  Require features
Open source and commercial offerings

## Slide 7: GCS - Software Options
Software | Runs on Linux | Runs on Windows | Runs on OSX
Mission Planner |  | YY | Y
MAVProxy | YY | Y | 
APM Planner 2 | YY | YY | YY
Qground control | Y | Y | YY
UgCS | YY | YY | YY

## Slide 8: GCS - Software Options
Software | Runs on Android | Runs on iOS
Tower | YY | 
MAVPilot |  | YY
SidePilot |  | YY
AndroPilot | YY | 

## Slide 9: GCS - Software Options
Compatibility and features vary widely between GCS programs

## Slide 10: GCS - MAVLink
Micro Air Vehicle Link
Standardised protocol for most open-source flight controllers
  Though some flight controllers may have extra MAVLink messages
Efficient and low datarate
Includes CRC to ensure validity of data
3 versions - 0.9, 1.0, 2.0
Arduplane can use 1.0 or 2.0 (default 1.0)

## Slide 11: GCS - MAVLink
Byte Index | Content | Value | Explanation
0 | Packet start sign | v1.0: 0xFE (v0.9: 0x55) | Indicates the start of a new packet.
1 | Payload length | 0 - 255 | Indicates length of the following payload.
2 | Packet sequence | 0 - 255 | Each component counts up his send sequence. Allows to detect packet loss
3 | System ID | 1 - 255 | ID of the SENDING system.
4 | Component ID | 0 - 255 | ID of the SENDING component.
5 | Message ID | 0 - 255 | ID of the message - the id defines what the payload “means” and how it should be correctly decoded.
6 to (n+6) | Data | (0 - 255) bytes | Data of the message, depends on the message id.
(n+7) to (n+8) | Checksum (low byte, high byte) | ITU X.25/SAE AS-4 hash, excluding packet start sign, so bytes 1..(n+6) | 

## Slide 12: GCS - MAVLink

## Slide 13: GCS - MAVLink

## Slide 14: GCS - MAVLink
There are MAVLink messages for sending/receiving parameters and missions
Typically, a flight controller may only send some of the messages - depending on it’s features, settings and current state

## Slide 15: GCS - MAVLink
MAVLink does include any encryption
  Up to the user to implement in their communications link
MAVLink 2.0 includes a “signing key”
  32-bit number
  Flight controller will only accept commands from packet signed with this key
  Disabled by default

## Slide 16: GCS - Flight Planning
Creating the waypoints to achieve the mission objectives

## Slide 17: GCS - Flight Planning
What is the mission objective?
  Primary and secondary goals
  Payload required
  UAV required
Most GCS software packages have a mission planning screen where you can drag-n-drop waypoints

## Slide 18: GCS - Flight Planning
Considerations
  Takeoff/landing area
  Hills/Terrain
  Flight altitude
  Mission length (km)
  Weather (wind)
  Communications coverage

## Slide 19: GCS - Flight Planning
If possible, run the mission in SITL beforehand, to ensure the waypoints are correctly laid out
Some GCS software packages have auto-generation of waypoints for mowing-the-lawn surveys

## Slide 20: Practical Session 1 (20min)
Create a mission that:
  Perform an aerial survey of the Snowy Hydro base
Considerations:
  Takeoff/landing at CMAC
  Landing will be manual
Create the mission, run in SITL
  cd ./ArduPlane
  ../Tools/autotest/sim_vehicle.py
Two options for GCS tool to use for mission planning (choose one)
  Connect Mission Planner via UDP, port 14550
  Use module load misseditor in MAVProxy

## Slide 21: GCS - Advanced Planning
Geofences
  A single closed polygon
UAV will turn back if it crosses outside of the polygon
  Note that the UAV’s inertia may send it beyond the fence for a short period

## Slide 22: GCS - Advanced Planning
Rally points
  Instead of a single Home point, have a set of rally points
  On RTL, the UAV will head to the nearest rally point

## Slide 23: GCS - Advanced Planning
Terrain Following
  Terrain data stored on Pixhawk’s SD card
  Arduplane will look at this database to estimate it’s AGL
  Available in AUTO, RTL and other flight modes. Will maintain a constant height above ground
  Set TERRAIN_ENABLE to 1 and TERRAIN_FOLLOW to 1
  Note the datasource is the SRTM data, so is only accurate to 20m

## Slide 24: GCS - Post flight analysis
Two types of logfiles
  GCS - saved copy of MAVlink stream (tlog)
  APM - saved on SD card (bin)
Bin log has more messages at a faster rate
  Generally the preferred log when analysing a flight
Tlog is on the GCS, so can be used if the UAV goes missing or is destroyed
  Still worth searching the crash site for the SD card!

## Slide 25: GCS - Post flight analysis
Tlogs are stored in:
  Mission Planner
    C:\Program Files (x86)\Mission Planner\logs
  MAVProxy
    Same folder that MAVproxy was run from (unless using the --aircraft option)

## Slide 26: GCS - Post flight analysis
Most flight analysis tools will work with both bin files and tlog files
Popular Flight Analysis tools:
  Mission Planner
  MAVExplorer (part of MAVProxy)

## Slide 27: GCS - Post flight analysis

## Slide 28: GCS - Post flight analysis
Mechanical Failures
  These appear in the log as a sudden divergence in the desired roll and pitch vs the vehicles actual roll and pitch

## Slide 29: GCS - Post flight analysis
Excessive Vibration

## Slide 30: GCS - Post flight analysis
Compass Interference
  Look for patterns between mag_field and throttle

## Slide 31: GCS - Post flight analysis
GPS Glitches

## Slide 32: GCS - Post flight analysis
Power brown-outs, if APM voltage varies by more than 0.15V, or goes below 4.7V

## Slide 33: Practical Session 2 (20min)
Logfile Analysis
  Find a logfile generated by SITL(./ArduPlane/logs) for the bin file
  For more interesting data: http://discuss.ardupilot.org/t/altitude-hold-and-stability/14536
Two options for Analysis tool (choose one)
  Mission Planner
  MAVExplorer
Check GPS
  GPS.Nsats and GPS.HDop messages
Check Vibration
  IMU.AccX, IMU.AccY, IMU.AccZ messages

## Slide 34: GCS - Inflight Monitoring
APM outputs a lot of telemetry data
How to watch all this in realtime?

## Slide 35: GCS - Inflight Monitoring
Decide which data is important
May vary depending on mission phase
  Speed, Altitude during takeoff and landing
  Moving map during mission

## Slide 36: GCS - Inflight Monitoring
Things to typically monitor
  Speed
  Altitude
  UAV Position (longitude/latitude) along with waypoints
  Battery voltage
  Telemetry link quality
  Any error messages
Anything that, if not detected in a short time, could result in a crash

## Slide 37: GCS - Inflight Monitoring
Have backup plans for common failure scenarios
Practice!
  In SITL
  In test flights
Consider having multiple GCS stations to split the workload

## Slide 38: The End!
Flight Planning
Logfile analysis
Inflight monitoring