## Slide 1: CanberraUAV Workshop Flight Controllers
Feb 2017

## Slide 2: Flight Controllers
Also known as Autopilot(s)
Take in information from sensors
Calculate the current state of the UAV
Compare this to where it’s supposed to be
Output that action to the engines and control surfaces

## Slide 3: Flight Controllers
Can have different levels of automation
  Stabilisation
  Waypoint-based navigation
  Full decision-making capability
May have failsafes for recovery from emergency situations

## Slide 4: Popular Flight Controllers
Open-source
  Ardupilot
  PX4
  Paparazzi
  Cleanflight
  KKMulticopter
  MultiWii
  Naze32

## Slide 5: APM History - Ardupilot
Also known as
  Arducopter/Arduplane/Ardurover
  APM
Capable of controlling many different types of vehicles
  Planes, Multicopters, Helicopters, Rovers, Boats, Submarines
Waypoint-based navigation
Advanced failsafe system
Highly configurable via (many!) parameters

## Slide 6: APM History - Ardupilot
Started in 2009 by Jordi Munoz, Doug Weibel, and Jose Julio
Designed to run on an Arduino board
Jordi Munoz and Chris Anderson went on to found 3D Robotics
Open source (GPL V3) project

## Slide 7: APM History - Hardware
Pixhawk 2(.1) (2016)
Arduino
ARM

## Slide 8: APM Basics - Ardupilot Organisation
Was previously funded by 3D Robotics
  3DR heavily used the Ardupilot software in their UAV’s
  Also sold many DIY parts
Was part of the Dronecode foundation
In early 2016, moved to the ardupilot.org non profit organisation

## Slide 9: Before we go any further…
All information if based on the current Arduplane release (3.5.2)
Some settings/parameters may be different for Arducopter/rover
Some settings/parameters may change in future releases of Arduplane

## Slide 10: APM Basics - Maintainers
Andrew Tridgell
  Vehicle: Plane, AntennaTracker
  Board: APM1, APM2, Pixhawk, Pixhawk2, PixRacer
Randy Mackay
  Vehicle: Copter, AntennaTracker
Robert Lefebvre
  Vehicle: TradHeli
Grant Morphett:
  Vehicle: Rover
Tom Pittenger
  Vehicle: Plane
Paul Riseborough
  Subsystem: AP_NavEKF2
Lucas De Marchi
  Subsystem: Linux
Peter Barker
  Subsystem: DataFlash
  Subsystem: Tools
Michael du Breuil
  Subsystem: uBlox GPS
Francisco Ferreira
  Bug Master
Matthias Badaire
  Subsystem: FRSky
Víctor Mayoral Vilches
  Board: PXF, Erle-Brain 2, PXFmini
Mirko Denecke
  Board: BBBmini
Georgii Staroselskii
  Board: NavIO
Emile Castelnuovo
  Board: VRBrain
Julien BERAUD
  Board: Bebop & Bebop 2
Pritam Ghanghas
  Board: Raspilot
Jonathan Challinger
  Vehicle: 3DRobotics Solo ArduPilot maintainer
Gustavo José de Sousa
  Subsystem: Build system
Craig Elder
  Administration: ArduPilot Technical Community Manager

## Slide 11: Ardupilot - HW vs SW
Ardupilot refers to the software
It can run on many different platforms
  Pixhawk
  BeagleBoneBlack
  Raspberry Pi
  X86
  Many different ARM-based boards
  (Arduino support has been dropped in recent versions)

## Slide 12: Ardupilot - HW vs SW
New hardware boards are being added regularly
Many variants of the Pixhawk platform in particular

## Slide 13: Ardupilot - Architecture

## Slide 14: Ardupilot - Architecture
Core Libraries
  AP_AHRS - attitude estimation using DCM or EKF
  AP_Common - core includes required by all sketches and libraries
  AP_Math - various math functions especially useful for vector manipulation
  AC_PID - PID controller library
  AP_InertialNav - inertial navigation library for blending accelerometer inputs with gps and baro data
  AC_AttitudeControl -
  AP_WPNav - waypoint navigation library
  AP_Motors - multicopter and traditional helicopter motor mixing
  RC_Channel - a library to more convert pwm input/output from APM_RC into internal units such as angles
  AP_HAL, AP_HAL_AVR, AP_HAL_PX4 - libraries to implement the “Hardware abstraction layer” which presents an identical interface to the high level code so that it can more easily be ported to different boards.

## Slide 15: Ardupilot - Architecture
Multithreaded (where supported) for low-level IO work and sensor drivers
Uses the AP_Scheduler library in the main vehicle thread

## Slide 16: Ardupilot - Architecture
2 Persistent Storage areas
  StorageManager
    Parameters
    Waypoints
    Geofence points
    Rally points
  DataFlash
    System log
    Are the *.bin files on the Pixhawk SD card

## Slide 17: Ardupilot - Sensors
Sensors provide information about the current state of the UAV
Different communications buses are supported
  I2C
  SPI
  UART
  CAN

## Slide 18: Ardupilot - Sensors
Gyro (I2C/SPI)
Accelerometer (SPI)
Magnetometer (I2C)
GPS (UART)
Power Sensor (I2C)
Barometer (I2C)
Pitot (I2C)
Laser Rangefinder (UART)
And more…
Support redundant sensors

## Slide 19: Ardupilot - Sensors
Sensors are auto-detected on startup
Hardware Abstraction Layer (HAL) separates the front and back end

## Slide 20: Ardupilot - Preflight Checks
System performs a check before arming
  Barometer
  Inertial (Gyro/Accel)
  Attitude solution (AHRS)
  Compass
  GPS
  Battery
  Airspeed
  Logging
  RC Control
  Safety switch
Will not arm if a check fails
  Checks can be disabled. Not recommended!

## Slide 21: Ardupilot - Compiling
Building the code into a single binary file
Different compilers needed for each hardware target
  G++ for Linux/Windows
  GCC-ARM (non-eabi) 4.9.7 or 5.9.3 for Pixhawk

## Slide 22: Ardupilot - Compiling
Ardupilot uses the “waf” make system
  waf --board=navio2 --targets =bin/arduplane
--board is the hardware target (sitl, px4-v1, etc)
--target is the airframe type (coax heli hexa octa octa-quad single tri y6 )
waf --help to get documentation

## Slide 23: Ardupilot - Compiling
Useful waf commands
waf list
  Lists all vehicle types (and other test programs)
waf list-boards
  Lists all board targets
waf clean
  Delete all files created during build
Also useful to add a -jx, where x is the number of threads to use in build

## Slide 24: Ardupilot - Uploading
To upload to a Pixhawk
  waf --upload /bin/arduplane
Mostly for working with the Pixhawk. Most other platforms (such as a Raspberry Pi) are a simple copy and paste

## Slide 25: Ardupilot - SITL
Software In The Loop
Runs Ardupilot attached to a flight simulator
  Jsbsim for Plane
  Custom simulators for copter, rover
  Can be attached to other simulators (Gazebo, Crrcsim, X-plane, etc)
Very useful for testing!

## Slide 26: Ardupilot - SITL

## Slide 27: Ardupilot - SITL
Ardupilot has a single script to build and run a SITL environment
  cd ardupilot/ArduPlane
  ../Tools/autotest/sim_vehicle.py

## Slide 28: Ardupilot - SITL
sim_vehicle options:
  -w Wipe and reset EEPROM to defaults
  -L <location> Start at a specific location (CMAC, Kingaroy, QMAC). Full list in ./Tools/autotest/locations.txt
  --console Use the MAVProxy console
  --map Enable to moving map
  -f <frame> Use a specific frame (+, X, quad or octa for Arducopter)

## Slide 29: Practical Session 1 (20min)
Configure WAF and build Arduplane
  cd ./ardupilot
  alias waf="$PWD/modules/waf/waf-light"
  waf configure --board=sitl
  waf --board=sitl --targets=bin/arduplane
Try building Arducopter
  waf --board=sitl --targets=bin/arducopter-quad

## Slide 30: Ardupilot - Mission
A mission is a set of waypoints that will be flown in auto mode
Missions are quite simple
  Go here, do that
No conditional statements or branching
  But can do loops
  Some exceptions (we’ll see later)

## Slide 31: Ardupilot - Waypoints
Simple text file
Each line is one waypoint
Can be
  Navigation commands
  Do auxiliary function
  Condition commands

## Slide 32: Ardupilot - Waypoints
File starts with line QGC WPL 110
Next line is the home location
Each line thereafter is a series of 12 tab-separated values
  Wp index number
  Current wp
  Coordinate frame
  The waypoint type
  Next 7 columns are the waypoint options
  Last column is autocontinue

## Slide 33: Ardupilot - Waypoints
Waypoint Type
16=Navigate to WP
22=Autotakeoff
177=Do Loop
X,Y,Z coords
Frame
0 = absolute altitude
3 = relative altitude

## Slide 34: Ardupilot - Waypoints
Popular waypoints
  MAV_CMD_NAV_WAYPOINT (Navigate to the specified position
  MAV_CMD_NAV_LOITER_TIME (Loiter at the specified location for a set time)
  MAV_CMD_NAV_RETURN_TO_LAUNCH (Return to the home location or the nearest Rally Point)
  MAV_CMD_DO_JUMP (Jump to the specified command in the mission list)

## Slide 35: Ardupilot - Waypoints
MAV_CMD_DO_SET_RELAY (Set a Relay pin’s voltage high (on) or low (off))
MAV_CMD_DO_SET_SERVO (Set a given servo pin output to a specific PWM value)
MAV_CMD_CONDITION_DISTANCE (Delay next DO_ command until less than x metres from next waypoint)
Plus many more…

## Slide 36: Ardupilot - Flight Modes
Many flight modes that give different mixes of user and computer controlled output
  MANUAL Complete manual control
  FLY BY WIRE_A (FBWA) Will hold roll and pitch
  AUTO Will run the mission stored in memory
  Return To Launch (RTL) Will return straight to home point
  LOITER Circle around current location
  … plus more modes

## Slide 37: Ardupilot - Failsafes
Failsafes are systems that take over control of the UAV if there is a perceived emergency
User configurable
Ensure you know which failsafes are active and:
  Under what condition they will activate
  Ardupilot’s resulting action(s)
  How to regain control

## Slide 38: Ardupilot - Failsafes
Short Failsafe
  Default 1.5 sec
  Choice of either Continue or circle
Long Failsafe
  Default 5 sec
  Choice of either Continue or RTL

## Slide 39: Ardupilot - Failsafes
RC Failsafe
  Activates at loss of signal from RC transmitter
  Requires RC TX/RX to be set up first, so it can signal Ardupilot on loss of signal
  Most recievers have a failsafe mode. Need to set this to output a low throttle value (<950 PWM)
GCS Failsafe
  Activates at loss of heartbeat packets from GCS

## Slide 40: Ardupilot - Failsafes
Battery voltage Failsafe
  Activates when battery reaches low voltage
Battery remaining Failsafe
  Activates when remaining battery charge (mAh) is reached

## Slide 41: Ardupilot - Failsafes
GPS
  There is not a GPS failsafe in Arduplane
  Plane will warn the user and attempt to dead-reckon

## Slide 42: Ardupilot - Failsafes
Geofence
  A set of points that define a closed polygon around the UAV
  Can have altitude limits
  Ardupilot Response can be:
    Ignore
    Report
    Take over control and return
  Disable for takeoff and landing!

## Slide 43: Ardupilot - Failsafes
There is an Advanced Failsafe System (AFS)
  Designed to comply to the rules of the UAV Challenge

## Slide 44: Practical Session 2 (20min)
Run sim_vehicle for a plane at CMAC, with default parameters, console and map
  cd ./ArduPlane
  ../Tools/autotest/sim_vehicle.py -w --console --map
Load a mission
  wp load ../Tools/autotest/ArduPlane-Missions/CMAC-toff-loop.txt
Run the mission in AUTO mode
  arm throttle
  auto
Type this in Cygwin console
Type this in MAVProxy console

## Slide 45: Ardupilot - Tuning
Each airframe has different responses to movements in it’s flight control surfaces
Ardupilot needs to take account of these responses for precise control
3 Controllers that require tuning
  PID (roll, pitch and yaw)
  L1 (horizontal navigation)
  TECS (height controller)
PID is the most important
  L1 and TECS defaults will cover most circumstances

## Slide 46: Ardupilot - Tuning
PID Controllers

## Slide 47: Ardupilot - Tuning
P
I
D

## Slide 48: Ardupilot - Tuning
PID tuning can be done manually or via autotune
  Manual: One person flies the UAV whilst the GCS operator monitors the roll/pitch response and changes the PID values
  Autotune: As above, but Ardupilot automatically measures the roll/pitch reponse and changes the PID values.

## Slide 49: Ardupilot - Tuning
Total Energy Control System (TECS)
  Coordinates throttle and pitch angle demands to control the aircraft’s height and airspeed
  Trading off demanded speed and demanded climb rate
  Complex tuning method

## Slide 50: Ardupilot - Tuning
L1 controller
  Controls horizontal turns both for waypoints and loiter
  Tuning the navigation controller usually involves adjusting one key parameter, called NAVL1_PERIOD
  Small value = sharp turns
  Large value = gentle turns

## Slide 51: Ardupilot - EKF
Extended Kalman Filter
  Algorithm to estimate vehicle position, velocity and angular orientation
  Take in measurements from all sensors (except rangefinder and pitot)
  “Fuses” the readings from the sensors together for an accurate solution
  Can reject readings with large errors
    Single sensor failure can be handled
  Does require a powerful CPU (>Arduino)

## Slide 52: Practical Session 3 (20min)
Start up Arduplane SITL
Load and run the same mission as last time
Vary the L1 controller in the MAVProxy console
  param set NAVL1_PERIOD n
  Where n is between 5 and 40 (default 20)
  Watch the effect on the turns
Vary the roll and pitch PID controllers in the MAVProxy console
  param set RLL2SRV_P n
  param set PTCH2SRV_P n
  Where n is between 0.1 and 4 (default 2.5)
  Watch the effect on the turns

## Slide 53: The End!
Ardupilot History
Ardupilot Architecture
  Sensors
  Libraries
Compiling and SITL
Controller tuning
Useful links
  http://ardupilot.org/plane/index.html
  http://ardupilot.org/dev/index.html
  http://discuss.ardupilot.org/